## Slide 1: DIGITAL ALARM CLOCK
STUDENT ID :
1705033
1705075

## Slide 2: Short Description :
We are going to design a simple digital Alarm clock using ATMEGA32 timers.
ATmega32A microcontroller has a 16 bit timer and we will be using that timer to count
the seconds and develop a digital clock.

## Slide 3: Hardware Required:
ATmega32 microcontroller
Crystal : All the digital clocks have a crystal inside of them which is the heart of clock. This crystal generates clock pulses, which is needed for timing calculations. For accuracy and higher frequency most prefer crystal based clock. We are going to connect a crystal of certain frequency to ATMEGA32 for getting accurate clock.
JHD_162ALCD(16x2 LCD) : To show the time on the LCD Display.

## Slide 4: Hardware Required:
Three pin switches : One Switch will be used for enabling adjust feature between alarm and time. There will be more buttons to increment or decrement MINUTE and HOUR.
Buzzer : Buzzer will automatically create sound at the alarm time set by the user.
Resistors
Capacitors
Power Supply (5V)

## Slide 5: Software Required:
Atmel Studio 7
Protues 8

## Slide 6: Working Principle :
The clock we choose here will be the frequency of crystal, let say F. If we use d Division Factor then every second we get F/d pulses. In ATMEGA there will be a 16 bit register , where we can store a value (compare value), when the counter counts up to the compare value an interrupt is set to generate.
We are going to set the compare value to F/d , so basically we will have a ISR (Interrupt Service Routine )on every comparison for every second. So we are going to use this timely routine to get the clock we needed.

## Slide 7: Motivation :
Time is the most precious resource because we can't get it back . So we want to measure it accurately.
Besides, alarm will alert us at our specified time to keep our sleep schedule regular. And they sometimes can be used for other remainder also.